## Slide 1: Processor Defense
Alex Penne
ECE350, Spring 2024
March 29, 2024

## Slide 2: Contents
Baby CPU
  pipelining structure, mult/div preparation
Hazardous CPU
  the terrible mult/div, early branching
Complete CPU
  easy bypassing, hard stalling
Testing and Bugs

## Slide 3: Baby CPU
making latches (DFFs)
  running numbers testbench
  pass through table (prevent extra decoding)
prepping for a mult/div stall
  add stalling to running numbers testbench
adding my alu
  running smoothly, minimal debugging
Latch | Pass Through Values
F/D | Current Insn, PC
D/X | Current Insn, PC, into ALU A, into ALU B, isMult, isDiv
X/M | Current Insn, PC, ALU Output, ALU Exceptions
M/W | Handled by Wrapper (data_writeReg, ctrl_writeReg, ctrl_writeEnable)

## Slide 4: Hazardous CPU
spent most time fixing mult/div
  fix mult/div_on signal latch
  latching mult/div_on wire
  enable DFF logic
  don’t skip an insn
  halt entire processor (will suck later)
early branching
  determine if branching in decode (more alus)
  if branch, insert only one nop
  more efficient cpu, more hardware needed

## Slide 5: Complete CPU
bypassing multiplexers
  used “one-hot” multiplexers
  got lucky with only needing 32-bit multiplexers (5-inputs)
  would change if more time
stalling changes
  needed stall that only stopped F/D, D/X (unlike mult/div)

## Slide 6: Testing and Bugs
made testbenches for every instruction
  used gradescope test cases to finalize (no long uploading)
passing all tests except for sort (0/10)
  stuck in a never-ending loop in malloc
  branch won’t bypass without skipping next instruction
  works for sort debug tests and branch bypassing tests
  if more time, would try and fix
solution: add nops when branching for final project